## Slide 1
UNITREE G1 · GROUP 2
Reach-and-touch
is now executable
Dry-run evidence and the path from our A3 DQN baseline to a learned multi-joint task
CSCN8020 · Final Project Dry Run
A3 trained policy evidence
Saved DQN checkpoint controlling the G1 left elbow

## Slide 2
We are extending a proven controller into a measurable task
2
01
A3 BASELINE
Control one joint
DQN selects decrease, hold, or increase for the left elbow target.
02
CURRENT DEMO
Validate the task
Scripted PD targets drive shoulder and elbow through reach, hold, and return.
03
FINAL POLICY
Learn the sequence
DQN or PPO will replace scripted targets and learn from task rewards.
→
→
The dry run proves the middle step; training remains the next milestone.

## Slide 3
The A3 DQN already provides a reliable learning baseline
3
20 / 20
greedy evaluation successes
100%
evaluation success rate
0.00491 rad
mean final absolute error reported for Config A

## Slide 4
Touch becomes a measurable RL objective
4
OBSERVATION
Joint angles and velocities
Hand and target positions
Hand-to-target error
Current task phase
ACTION
Discrete target changes
for shoulder and elbow
Initial baseline stays
compatible with DQN
SUCCESS
Distance ≤ target radius
and hold duration ≥ threshold
Return to neutral pose
is evaluated separately
rₜ = − ‖p_hand − p_target‖₂ + b_touch − λ · smoothness
Reward closer motion, sustained contact, and stability while penalizing unnecessary oscillation.

## Slide 5
The demo validates one complete reach-touch-return cycle
5
REST
Stabilize the robot
→
REACH
Interpolate arm targets
→
TOUCH / HOLD
Stay inside the target
→
RETURN
Recover neutral pose
target-radius = 0.045 m
The hand is touching when endpoint distance is within 4.5 cm.
required-hold = 1.5 s
The run succeeds only after enough contact time accumulates during TOUCH/HOLD.

## Slide 6
The demo succeeds with 1.2 mm endpoint accuracy
6
Chart: Endpoint distance across the four phases
| 0.0 | 0.5 | 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0 | 5.5 | 6.0 | 6.5 | 7.0 | 7.5 | 8.0 | 8.5 | 9.0
Hand-to-target distance (m) | 0.22914 | 0.22914 | 0.22914 | 0.22193 | 0.19059 | 0.14151 | 0.082947 | 0.030389 | 0.0034731 | 0.0023551 | 0.0019481 | 0.0016116 | 0.0013223 | 0.0092366 | 0.054268 | 0.11329 | 0.16864 | 0.20876 | 0.22752
0.0012 m
minimum endpoint distance
2.002 s
accumulated touch time
SUCCESS
Headless verification and the visual demo use the same thresholds.

## Slide 7
The demo proves task mechanics, not learned behavior
7
PROVEN NOW
✓ Multi-joint arm actuation
✓ Virtual target visualization
✓ Endpoint-distance measurement
✓ Touch and hold success rule
✓ Reach, hold, and return phases
✓ Reproducible CSV evidence
STILL TO LEARN
○ Action selection from observations
○ Reward-driven policy improvement
○ Robustness across target positions
○ Comparison against scripted baseline
○ Motion smoothness under DQN or PPO
○ Held-out multi-seed evaluation
This distinction keeps the dry-run claim accurate and gives us a clean experimental baseline.

## Slide 8
Next, the learned policy must beat the scripted baseline
8
01
Environment
Expose state, discrete actions, reward, and termination through Gymnasium.
02
Training
Train DQN across randomized reachable targets and tune reward weights.
03
Evaluation
Report success rate, distance, hold time, reward, and smoothness over fixed seeds.
04
Decision
Keep DQN if motion is stable; compare PPO if discrete control remains jerky.
Dry-run ask
Confirm the task definition and evaluation criteria before full training.