## Slide 1
CSCN8020 FINAL PROJECT
Unitree G1 Actor-Critic
Reach-and-Touch
Project Progress Report
Group 2
Haibo Yuan | Ce Chen | Zhuoran Zhang
A learned policy that adapts to different reachable targets

## Slide 2
— CURRENT IMPLEMENTATION
02
The learned policy now reaches different blue targets
Current milestone
PPO Actor-Critic controls the left arm while the Inspire hand remains in a validated pointing pose.
Target-conditioned behavior
A new reachable 3D target is generated each episode and included in the state.
100/100
Independent successes
randomized evaluation targets
0.0185 m
Mean minimum distance
touch tolerance = 0.045 m
4
Controlled arm joints
continuous Actor actions
Evidence
Saved checkpoint selected at PPO update 35; deterministic evaluation uses separate seeds.
Scope boundary
This is a kinematic reaching baseline with virtual touch, not torque control or detailed physical contact.
The target changes, the state changes, and the Actor produces a different joint trajectory.

## Slide 3
— WHAT THE ROBOT LEARNS
03
The Actor learns a target-conditioned reaching policy
Observe
Robot joints, fingertip,
blue target and relative error
Act
Four continuous joint-position
increments from the Actor
Evaluate
Critic estimates V(s) and
PPO computes an advantage
Improve
Increase probability of actions
that produce higher return
sₜ
→
aₜ ~ πθ(a|sₜ)
→
rₜ , sₜ₊₁
→
δₜ
Learning means the same saved Actor can reach different targets because target position is part of its input.

## Slide 4
— MDP DEFINITION
04
The state explicitly describes the robot and its target
State sₜ = [ qₜ, q̇ₜ, pᵗⁱᵖₜ, pᵗᵃʳᵍᵉᵗ, Δpₜ, dₜ, hₜ ] ∈ ℝ¹⁹
qₜ ∈ ℝ⁴
Controlled joint angles
q̇ₜ ∈ ℝ⁴
Controlled joint velocities
pᵗⁱᵖ, pᵗᵃʳᵍᵉᵗ ∈ ℝ³
Fingertip and blue-target positions
Δpₜ ∈ ℝ³
Target minus fingertip
dₜ = ‖Δpₜ‖₂
Euclidean fingertip distance
hₜ ∈ [0,1]
Normalized touch-hold progress
Including pᵗᵃʳᵍᵉᵗ and Δpₜ is what lets the policy react when the blue target moves.

## Slide 5
— ACTOR-CRITIC LEARNING LOOP
05
Actor and Critic improve together through PPO
State sₜ
19-value observation
Actor πθ
selects action aₜ
MuJoCo
returns rₜ, sₜ₊₁
Critic Vφ
estimates state value
PPO update
improves θ and φ
→
→
→
→
Training
Stochastic Gaussian actions
PPO clipped policy update
Evaluation
Deterministic Actor mean
No exploration and no retraining
The Actor chooses actions; the Critic supplies the learning signal. They are not DQN online and target networks.

## Slide 6
— MATH TO CODE
06
PPO turns Critic estimates into an Actor update
TD error
δₜ = rₜ + γVφ(sₜ₊₁) − Vφ(sₜ)
Generalized advantage
Âₜ = δₜ + γλδₜ₊₁ + ⋯
Clipped Actor objective
Lᴾᴾᴼ = −min(ρₜÂₜ, clip(ρₜ)Âₜ)
Implementation
action, log_prob, value = actor_critic.act(state)
delta = reward + gamma * next_value - value
advantages, returns = generalized_advantage_estimate(...)
ratio = exp(new_log_prob - old_log_prob)
actor_loss = -min(ratio * advantage, clipped * advantage)
critic_loss = 0.5 * (return - value)²
The Critic learns V(s); its advantage estimate tells the Actor which target-conditioned actions performed better than expected.

## Slide 7
— RESULTS AND EVIDENCE
07
The selected policy succeeds on 100 unseen target episodes
100/100
Evaluation successes
seeds 1000–1099
0.0185 m
Mean minimum distance
well within 0.045 m tolerance
35
Selected PPO update
best validation checkpoint
0.045 m
Touch tolerance
8 consecutive steps
Validation success during training
Chart: PPO update
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40
Validation success (%) | 40 | 0 | 70 | 100 | 100 | 100 | 100 | 100
What the evidence means
• The checkpoint reloads without retraining.
• Every evaluation seed produces a different reachable target.
• Success requires sustained fingertip proximity, not a single close frame.

## Slide 8
— LIMITATIONS AND NEXT STEPS
08
The current policy proves adaptation, with clear physical limits
Completed
• Five-finger Inspire model
• Randomized reachable targets
• PPO Actor and Value Critic
• Saved-model evaluation
Current limitations
• Kinematic joint increments
• Virtual distance-based touch
• Pointing hand is fixed
• Target moves between episodes
Next engineering steps
• Cartesian target input
• Mid-episode target movement
• Dynamic/torque controller
• Simplified physical contact
Question for feedback
Is this target-conditioned kinematic baseline an appropriate foundation before introducing torque control and physical contact?

## Slide 9
— LIVE DEMO
09
The saved Actor now follows five different blue targets
Run command
macOS $ mjpython final_project/evaluate_actor_critic.py --episodes 5 --viewer
Windows/Linux $ python final_project/evaluate_actor_critic.py --episodes 5 --viewer
1
Checkpoint loaded
PPO update 35
2
Blue target moves
new target each episode
3
Actor controls arm
four continuous actions
4
Touch is measured
distance, reward, success
Watch the blue target change, the fingertip distance fall, and TOUCH SUCCESS appear without retraining.