## Slide 1
UNITREE G1 + INSPIRE · GROUP 2
Five-finger pointing
is now executable
An articulated Inspire-hand baseline with fingertip-level success measurement
CSCN8020 · Final Project Dry Run
A3 learning baseline
Earlier checkpoint evidence; Inspire demo follows live
Notes: Open by naming the scope precisely: this is an executable Inspire five-finger scripted baseline, not a trained reach-and-touch policy. The actual modeled left index fingertip is the endpoint.

## Slide 2
The Inspire demo connects our proven DQN to a richer task
2
01
A3 BASELINE
Learn one joint
DQN selects discrete changes for the left-elbow target.
02
INSPIRE DEMO
Validate the hand
Scripted joint targets drive the left arm and articulated fingers.
03
ADAPTIVE POLICY
Generalize targets
IK first, then DQN or PPO across reachable target positions.
→
→
The dry run validates mechanics; adaptation and training remain next.
Notes: Explain the three stages. A3 proved DQN infrastructure. This Inspire demo validates articulated-hand mechanics. The next stage adds target adaptation and then policy learning.

## Slide 3
The A3 DQN still provides our learning foundation
3
20 / 20
greedy evaluation successes
100%
evaluation success rate
0.00491 rad
mean final absolute error reported for Config A
Notes: Use the A3 numbers only as evidence that our DQN training and evaluation pipeline works. Do not claim these elbow-only results prove the new five-finger task.

## Slide 4
The endpoint is now an actuated index fingertip
4
MODEL
53 modeled joints
29 body + 24 hand joints
Left Inspire hand articulated
Right side visually simplified
CONTROL NOW
7 left-arm targets
12 left-finger targets
Deterministic scripted
joint-position baseline
MEASUREMENT
Actual index-tip site
Distance ≤ target radius
Hold ≥ threshold
and complete the sequence
Planned RL: rₜ = − ‖p_tip − p_target‖₂ + b_touch − λ · smoothness
The scripted baseline validates every signal required by the future RL objective.
Notes: Point out the 53-joint model: 29 body joints plus 24 hand joints. The baseline commands seven left-arm and twelve left-hand targets. The planned RL objective will use fingertip distance, touch reward, and smoothness.

## Slide 5
Six phases produce one complete point-touch-return cycle
5
REST / POINT
Relax, then shape the fingers
→
REACH
Move the actual fingertip
→
TOUCH / HOLD
Accumulate valid contact time
→
RETURN / RELAX
Return arm and open hand
target-radius = 0.045 m
The index-tip site must remain within 4.5 cm of target centre.
required-hold = 1.5 s
At least 1.5 s must accumulate during TOUCH/HOLD.
Notes: Walk through REST, POINT, REACH, TOUCH/HOLD, RETURN, and RELAX. Define target-radius as the allowed centre distance and required-hold as accumulated valid time.

## Slide 6
The Inspire baseline reaches the target and holds
6
Chart: Index-tip distance across the six phases
| 0.0 | 0.5 | 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0 | 5.5 | 6.0 | 6.5 | 7.0 | 7.5 | 8.0 | 8.5 | 9.0
Hand-to-target distance (m) | 0.19883 | 0.19883 | 0.19883 | 0.19883 | 0.19775 | 0.17332 | 0.11864 | 0.048686 | 0.0023622 | 0 | 0 | 0 | 0.019261 | 0.083286 | 0.14909 | 0.18934 | 0.19883 | 0.19883 | 0.19883
0.0000 m
minimum index-tip distance
2.002 s
accumulated touch time
SUCCESS
Visual and headless runs use the same fingertip endpoint and thresholds.
Notes: State the verified headless result: minimum distance 0.0000 m, touch time 2.002 s, success=True. These are fixed-target scripted results, not learned accuracy.

## Slide 7
This demo validates mechanics only
7
PROVEN NOW
✓ Articulated five-finger model
✓ Actual index-tip endpoint
✓ Natural point gesture
✓ Six-phase task sequence
✓ Touch-and-hold criterion
✓ Reproducible CSV evidence
STILL TO LEARN
○ Adapt to a moved target
○ IK or policy action selection
○ Reward-driven improvement
○ Multiple target positions
○ DQN/PPO baseline comparison
○ Held-out multi-seed evaluation
Today the target is fixed from TOUCH_ARM; moving it requires IK or a learned controller.
Notes: Be explicit about the boundary. We have validated the model, endpoint, gesture, task phases, thresholds, and metrics. The arm does not yet adapt if the target moves.

## Slide 8
Next, make the fingertip adapt before full RL training
8
01
Environment
Expose fingertip error, actions, reward, and termination through Gymnasium.
02
Adaptation
Add IK so the arm responds when target position changes.
03
Training
Train DQN or PPO across randomized reachable targets.
04
Evaluation
Compare success, distance, hold time, reward, and smoothness.
Dry-run ask
Confirm the Inspire task scope before adaptive control and training.
Notes: Close with the sequence: expose Gymnasium signals, add IK for target adaptation, train DQN or PPO, and evaluate against this scripted baseline. Ask whether the task scope is appropriate.